## Slide 1: Python Drivers
Robotics Bootcamp 2026

## Slide 2: Outline of Today
Introduction to Robots and robot types
Meet our robots
Lab safety
Install/go over Python drivers
LUNCH
Brief Lab Tour
Teaching Pendant Lab
Python Lab
  If extra time: switch robots
We are here.

## Slide 3: Why use Python drivers?
TP programs are limited in what they can do
Still used a lot in industry, but still limited
Python provides flexibility
  Machine Vision integration
  Inter-robot communication
  Etc...

## Slide 4: How does it work?
The robot TP runs a program continuously reading and updating its registers.
The Python program sets movement/gripper registers and handles all logic.
Python writes to robot controller registers via Ethernet-IP.

## Slide 5: FANUC Driver
Navigate to the Github repository:
https://github.com/laceyhunt/robots_bootcamp_2026/tree/master
Clone it (or download as a ZIP) and open it
Activate your Python environment and run:
pip3 install pycomm3 OR conda install pycomm3

## Slide 6: StdBot Driver
Open the 'standard_bot' folder in the terminal
Ensure a python virtual environment (conda, venv, etc.) is active
Run 'pip install –r requirements.txt'
Open 'standard_bot.py' in Visual Studion Code
The folder contains several files:
  Standard_bot.py
  Get_pose.py
  Requirements.txt
  Positions.py

## Slide 7: After Lunch Lab 1: TP
Whichever Robot you choose to work with, you will first make a TP program to...
Go to home location
Pick up a die
Move the die
Place die somewhere new
Return home

## Slide 8: After Lunch Lab 2: Python
Home Robot
Pick up die
Place on conveyor
Turn on conveyor
Stop conveyor once die reaches proximity sensor
Pick up die
Place die back at start
Go back home

## Slide 9: When we are down there, log into WiFi
Network: CDA Robot
Password: 12345678

## Slide 10: Outline of Today
Introduction to Robots and robot types
Meet our robots
Lab safety
Install/go over Python drivers
LUNCH
Brief Lab Tour
Teaching Pendant Lab
Python Lab
  If extra time: switch robots
We are here.