## Slide 1: Robots Intro
Robotics Bootcamp 2026

## Slide 2: Instructor Background
Lacey Bowden
CS Masters Student
  Masters Topic: Industrial Robotics
NIC Fellow
Kevin Wing
CS PhD Student
  Masters Topic: Agriculture IoT Device
  PhD Topic: Genetic Algorithms/Optimization with AI

## Slide 3: Outline of Today
Introduction to Robots and robot types
Meet our robots
Lab safety
Install/go over Python drivers
LUNCH
Brief Lab Tour
Teaching Pendant Lab
Python Lab
  If extra time: switch robots
We are here.
Upstairs Downstairs

## Slide 4: What is a robot?
At the highest level: a computer and an actuator.
A computer accepts raw data as input, processes it using stored instructions (software), stores the results, and produces output.
An actuator converts energy—typically electric, hydraulic, or pneumatic—into mechanical motion to move or control something.

## Slide 5: In other words...
The computer performs operations, the actuator interacts with the world somehow.
Look at this washing machine...

## Slide 6: Some more examples

## Slide 7: Some robot types
There are many types of robots. Today, we are going to look at and discuss these five types:
Humanoid Robots
Gantry Robots
SCARA Robots
Articulated Robots
Cobots

## Slide 8: Humanoid Robots
This is often what people picture...
These robots are designed to reflect humans
  Bipedal (two feet)
  Sensing
  Vision
In theory, these are great (because humans are great)
  We are low-power, high-efficiency
https://robostore.com/cdn/shop/files/unitree-g1-edu-ultimate-a-robotic-humanoid-u3-8215619.jpg?v=1759440110&width=2000

## Slide 9: Humanoid Robots
Similar to this is the quadruped (four-legged) robot dog

## Slide 10: Humanoid Robots
What are some limitations of this type of robot?
https://robostore.com/cdn/shop/files/unitree-g1-edu-ultimate-a-robotic-humanoid-u3-8215619.jpg?v=1759440110&width=2000
  Sensory input requirements
  Power
  Balance
  Battery Life
  Etc...

## Slide 11: Humanoid Robots
What are some limitations of this type of robot?
  Sensory input requirements
  Power
  Balance
  Battery Life
  Etc...
https://www.youtube.com/shorts/jvQdFe8FPCw

## Slide 12: Other types
There are many other types of robots. Today, we are going to look at and discuss these five types:
Humanoid Robots
Gantry Robots
SCARA Robots
Articulated Robots
Cobots

## Slide 13: Gantry Robots
Gantry Robots (or Cartesian Robots)
Move along a 3-axis linear coordinate system
  X, Y, and Z
Example: Computer Numeric-Controlled (CNC) machines
https://www.macrondynamics.com/wp-content/uploads/2023/03/Gantry-Systems-Working-Outside-and-Envelope.jpg

## Slide 14: Gantry Robots
Great for subtractive (milling) or additive (3D printing) manufacturing

## Slide 15: Gantry Robots
Also for traversing and monitoring some plane

## Slide 16: Gantry Robots
What are some limitations of this type of robot?
https://www.macrondynamics.com/wp-content/uploads/2023/03/Gantry-Systems-Working-Outside-and-Envelope.jpg
  Curved surfaces
  Limited by end of arm tool
  Large footprint
  Etc...

## Slide 17: Other types
There are many other types of robots. Today, we are going to look at and discuss these five types:
Humanoid Robots
Gantry Robots
SCARA Robots
Articulated Robots
Cobots

## Slide 18: SCARA Robots
Selective Compliance Articulated Robot Arms (SCARA) robots
High-speed, high-precision, excellent repeatability
Four axes
https://upload.wikimedia.org/wikipedia/commons/0/09/SCARA_robot_2R.png

## Slide 19: SCARA Robots
Used for assembly, palletizing, packaging, pick-and-place, etc.

## Slide 20: SCARA Robots
What are some limitations of this type of robot?
https://upload.wikimedia.org/wikipedia/commons/0/09/SCARA_robot_2R.png
  Short reach
  Light payload
  Limited by three planes of movement, can't work with curved surfaces
  Etc...

## Slide 21: Other types
There are many other types of robots. Today, we are going to look at and discuss these five types:
Humanoid Robots
Gantry Robots
SCARA Robots
Articulated Robots
Cobots

## Slide 22: Articulated Robots
Articulated robots are arms with rotary joints
  Rotary joints are connection points allowing rotational movement around a single axis, acting like a human joint (shoulder, elbow, wrist)
Typically four to seven joints (or axes)
  Six is probably most common
https://d16ohktstcjvly.cloudfront.net/image/513891251684/image_2jpmakctih2bd5pq8eo0d5l60d/-T1%3A1.2-FJPG

## Slide 23: Articulated Robots
These robots are often controlled one of two ways:
First, by sending degree values to each axis in a list like this:
[0, 0, 0, 0, 0, 90]
Or
[0, 0, 90, 0, 0, 90]
This is called joint movement
  But we often don't think of space like this...
https://docs.quanser.com/quarc/documentation/kuka_axes.gif

## Slide 24: Articulated Robots
So, most articulated robots also offer cartesian movements, which allow us to pass x, y, z coordinates, and the robot calculates the joint values to get there.
Like this:
[600, 100, 50, -180, 0, 180]
Note: from end of arm, often in millimeters
https://education.vex.com/stemlabs/sites/default/files/inline-images/Screen%20Shot%202023-11-08%20at%201.09.12%20PM%20%282%29.png
X Y Z

## Slide 25: Side Note: Right Hand Rule
The Right-Hand-Rule (RHR) can help us with programming robot movement.
https://automaticaddison.com/wp-content/uploads/2024/11/2-right-hand-rule-of-robotics.jpg

## Slide 26: Articulated Robots
So, most articulated robots also offer cartesian movements, which allow us to pass x, y, z coordinates, and the robot calculates the joint values to get there.
Like this:
[600, 100, 50, -180, 0, 180]
Note: from end of arm, often in millimeters
https://education.vex.com/stemlabs/sites/default/files/inline-images/Screen%20Shot%202023-11-08%20at%201.09.12%20PM%20%282%29.png
X Y Z
...but what are these?

## Slide 27: Articulated Robots
With cartesian movements, we pass x, y, and z and something called Euler Angles
[600, 100, 50, -180, 0, 180]
The Euler Angles define the tool's orientation
  The rotation around each axis
https://education.vex.com/stemlabs/sites/default/files/inline-images/Screen%20Shot%202023-11-08%20at%201.09.12%20PM%20%282%29.png
X Y Z
Euler Angles
Yaw Pitch Roll

## Slide 28: Articulated Robots
With cartesian movements, we pass x, y, and z and something called Euler Angles
[600, 100, 50, -180, 0, 180]
The Euler Angles define the tool's orientation
  The rotation around each axis
X Y Z
Euler Angles
Yaw Pitch Roll
https://www.researchgate.net/figure/a-Pitch-yaw-and-roll-angles-of-an-aircraft-with-body-orientation-O-u-v-original_fig7_348803228

## Slide 29: Articulated Robots
Singularities are points in space where these rules of movement break down, and we try to send a robot to a place it physically cannot go
These most often occur with articulated robots
  Example: what if I try to send this coordinate value?
  [0,0,0,0,0,0]
https://education.vex.com/stemlabs/sites/default/files/inline-images/Screen%20Shot%202023-11-08%20at%201.09.12%20PM%20%282%29.png

## Slide 30: Articulated Robots
As with most robots, an end-of-arm tool (EOAT) is added to the end to increase functionality
  Often, but not limited to, a gripper
https://toolbox.igus.com/wp-content/uploads/2023/10/end-effectors-in-robotics.png
https://www.emicorp.com/media/catalog/product/cache/0daeb07bb1d294c1f281fab47369d56a/l/g/lg-8201.jpg
https://www.tthk.ee/inlearcs/wp-content/uploads/2020/11/Picture-72.png
https://millibar.com/wp-content/uploads/vacuum-pick-head-for-aluminum-tubes-18x2-inch-aluminum-extension-millibar-custom-end-of-arm-tooling-600px.jpg

## Slide 31: Articulated Robots
We will be using this type of robot in lab this week
  Specifically, the FANUC CRX-10

## Slide 32: Articulated Robots
https://d16ohktstcjvly.cloudfront.net/image/513891251684/image_2jpmakctih2bd5pq8eo0d5l60d/-T1%3A1.2-FJPG
What are some limitations of this type of robot?
  Specialized programming
  Singularities
  Unpredictable path
  Etc...

## Slide 33: Other types
There are many other types of robots. Today, we are going to look at and discuss these five types:
Humanoid Robots
Gantry Robots
SCARA Robots
Articulated Robots
Cobots

## Slide 34: Cobots
Finally, Collaborative Robots (cobots for short) are robots that are safe for humans to work around without protective cages
They have safety sensors in each joint that detect resistance and stop all movement if it crosses some threshold
  They are not 100% safe, you can still hit your head and they can still drop things
  But much safer than no sensing at all

## Slide 35: Other types
There are many other types of robots. Today, we are going to look at and discuss these five types:
Humanoid Robots
Gantry Robots
SCARA Robots
Articulated Robots
Cobots